What is a chord?
- Several notes that sound simultaneously.
  - 2 notes: dyad
  - 3 notes: triad
  - 4 notes: tetrad
- What’s a note?
  - A named pitch: A, B, C…
- What’s a pitch?
  - A sound in a certain frequency: A=440 Hz, C=261 Hz

---
What is a chroma? 1/2
- All pitches equally spaced in frequency domain, belongs to the same Pitch Class.
- A pitch can be separated in two components: tone height and chroma.
- A Chroma is a way to categorize pitches from the same Pitch Class.
  - C2 and C5 both have the same chroma value C
All C from C1 to C7

---
What is a chroma? 2/2
A Chromagram shows the presence of all chromas in an audio signal for a given time window.

---
Objective
For a given audio signal, compute and display the chroma values found.

---
Compute pitch
- Use a predefined filter bank to decompose signal in 88 sub-bands. (MIDI 21 to 108)
- On each MIDI pitch compute the STMSP
- Save the result in an array and return

---
Decomposing the signal
- Predefined filters created by paper’s authors.
- Band pass filter for
  A4 = 440 Hz

---
Pitches detected
MIDI bands

---
Pitches colormap
MIDI 60
C4

---
Chroma detection
- The first chord is identified correctly.
- The notes marked in red were wrong
- Am in yellow seems to be correct.
Am
G
F
C

---
Trying sample audio
A scale C to B identified correctly